## Slide 1: A Calibration Method for Optical See-through Head-mounted Displays with a Depth Camera
Hanseul Jun Gunhee Kim
March 19, 2016

## Slide 2
Problem Statement
Approach
  Mathematical Model
  Optimization Formula
Experiments
Conclusion
Outline

## Slide 3: User wearing an OST-HMD
Suppose that a user is wearing a OST-HMD
User expects virtual objects to coexist with the real objects
Wrong positions of virtual objects lead to annoyance
Notes: https://www.flickr.com/photos/smieyetracking/20344061815
https://www.flickr.com/photos/overig/4639331740
https://en.wikipedia.org/wiki/File:Augmented_reality_world_globe.png

## Slide 4: User wearing an OST-HMD
Suppose that a user is wearing a OST-HMD
Since human visual systems are complex, we can not directly measure how the positions are wrong
Can we put the virtual objects in the right places?

## Slide 5: Previous Calibration Methods
Methods with User Interactions
[Itoh et al., 3DUI 2014]
[Kellner et al., TVCG 2012 ]
[Plopski et al., TVCG 2015 ]
[Genc et al., ISAR 2000]
Many more!
Methods without User Interactions
[Owen et al., ISMAR 2014 ]

## Slide 6: Limitations of Previous Works
Methods with User Interactions
Methods without User Interactions
Perceptual eye centers are not identical to the anatomical eye centers with additional devices
Long user interaction time with additional devices
Our goal: a perceptual and handy approach to calibration without any additional devices
Notes: Arthur Tang et al., Evaluation of Calibration Procedures for Optical See-Through Head-Mounted Displays

## Slide 7: Definition of Calibration
Mathematical Definition: figure out all user and device dependent parameters
Parameter 1: Depth-camera Extrinsic Parameter
Naive Definition: put all virtual objects in the intended places
Parameter 3: User Eye Positions
Parameter 2: Display Extrinsic Parameter

## Slide 8: Our Goals
Objective: calibrate an OST-HMD for a user
Goal 2: calibrate an OST-HMD with a small amount of practical user interaction
Goal 3: calibrate an OST-HMD without additional devices
Goal 1: calibrate an OST-HMD for a user with a perceptual model

## Slide 9: Our Solution
Calibration with a Depth-camera
(1) Perceptual Model without anatomical eye position estimation
(2) Fingertips for user interaction
(3) Depth-cameras for detection

## Slide 10: How to Calibrate?
A set of positions of a user’s fingertip for a set of virtual targets
How to know the intention of the users?
Infer user intentions through pointing correct positions
Users unconsciously know how to calibrate but do not know how to deliver the information
Pointing the correct positions does deliver the information

## Slide 11
Problem Statement
Approach
  Mathematical Model
  Optimization Formula
Experiments
Conclusion
Outline

## Slide 12: Overview of Model
Represents the system of a depth camera, a OST-HMD, and an user with a transformation A
2 coordinate systems
  : depth-camera and eye
1 transformation
  : a translation, a rotation, and an isotropic scaling

## Slide 13: Overview of Model
Transformation A is inferred through the positions of virtual targets pointed by an user
p: pointed positions in the depth-camera coordinate system
v: intended positions of virtual targets

## Slide 14: Components of Transformation A
Camera
Displays
User Eyes
T + R + S
T + R
A
(T) Camera position
(R) Camera rotation
(T) Eye position
(R) Eye rotation
(S) Interpupillary distance (IPD)
Notes: v=[]v_i 굵게 해보기 (다음장과 통일)

## Slide 15: Components of Transformation A
Discrepancy between the actual IPD and the initialized IPD results in an isotropic scaling
(Isotropic scaling of )
: actual IPD
: initialized IPD

## Slide 16
Problem Statement
Approach
  Mathematical Model
  Optimization Formula
Experiments
Conclusion
Outline

## Slide 17: Optimization Objective
Uses component-wise interpretation of Transformation A
, where
componentize
obtain the objective
Without a known : Full Calibration
With a known : Simplified Calibration
Notes: Obtain the objective 화살표가 || ||를 가리키도록
2페이지로 나눠볼 것
아래쪽 표 뒤에도 나오니까 지워보는 것 고려

## Slide 18: Optimization Objective
obtain the objective
where
,
Optimize Transformation A with pairs of p and v
(the above formula historically comes from [Horn, JOSA A 1987])

## Slide 19: Degree of Freedom (DOF)
Without a known : Full Calibration
With a known : Simplified Calibration
Optimization quality
DOF
Less DOF
Better Optimization
Reuse stable Rotation for better calibration

## Slide 20
Problem Statement
Approach
  Mathematical Model
  Optimization Formula
Experiments
Conclusion
Outline

## Slide 21: Experiment Criteria
Gather 3D position error:
Divide it (calibration error + non-calibration error):
Apply law of large numbers (assume Gaussian):
Extract calibration error:
Criterion 1: smaller calibration errors = better calibration
How to get calibration errors?
Criterion 2: smaller number of interactions = better calibration

## Slide 22: Experiment Setup
Hardware: Meta 1
  Affordable Price: $667
  960x540 resolution displays
  320x240 resolution depth-camera
Subjects: 20 people not familiar to OST-HMDs
depth-camera
Baseline: stereo-SPAAM [Genc et al., ISAR 2000]
  Modified to work better for depth-cameras

## Slide 23: Quantitative Results
Measured 3D calibration position errors
  Used mean absolute errors (MAE) of the subjects
Used mean absolute errors to tell the proper number of interactions
To achieve <1 cm, >11 (full) and >8 (simplified) recommended.

## Slide 24: Qualitative Results
Our method well aligns the left and right displays
  Our calibration model handles both displays at the same time
  Better alignment improves user experiences

## Slide 25: Non-calibration Error Distribution
Supports our assumption of Gaussian distribution
  Validates our calibration error extraction step 3
  The variation is larger along the z-axis since it comes from disparity, that makes it more vulnerable to errors

## Slide 26
Problem Statement
Approach
  Mathematical Model
  Optimization Formula
Experiments
Conclusion
Outline

## Slide 27: Conclusion
Our calibration method
utilizes depth camera commonly included in HMDs.
works with a small number of interactions.
results with aligned displays.
works for novice users with affordable HMDs.

## Slide 28: Thank you!